## Slide 1
Circuit-01:General PMOS–NMOS High-Side Driver
Introduction
A high-side switch connects or disconnects the positive supply from a load. In this design, a PMOS transistor acts as the high-side switch, while an NMOS transistor is used as a gate driver. Since the PMOS source is connected to a 100 V DC supply, the 3.3 V controller cannot directly drive the PMOS gate. Therefore, the NMOS provides level shifting by pulling the PMOS gate towards ground whenever the control signal is HIGH. A 12 V Zener diode is connected between the gate and source of the PMOS to clamp the gate-to-source voltage within its safe operating limit.
Working Principle - OFF Condition (Logic Input = 0 V)
  The NMOS transistor remains OFF
  No current flows through the NMOS
  The pull-up resistor keeps the PMOS gate at the same potential as the source (100 V)
  Therefore, VGS = 0 V
  Since the gate-to-source voltage is zero, the PMOS remains OFF and no current flows through the load
Working Principle - ON Condition (Logic Input = 3.3 V)
  The NMOS transistor turns ON
  The PMOS gate is pulled towards ground through the NMOS
  The Zener diode clamps the gate voltage to approximately 12 V below the source
  Therefore, VGS ≈ −12 V
  This gate voltage is sufficient to fully enhance the PMOS, allowing the full 100 V supply to appear across the load
Main Components
  PMOS transistor – High-side power switch
  NMOS transistor – Gate driver
  Zener diode (12 V) – Gate protection
  R1 – Zener bias resistor
  R2 – Gate pull-up resistor
  C1 – Noise suppression capacitor
Circuit Diagram Area
Space reserved for circuit diagram insertion
Notes: 1

## Slide 2
Circuit Design and Component Calculations
Design Specifications Table:
Parameter
Value
High Voltage Supply
100 V
Logic Input
3.3 V
Zener Voltage
12 V
Desired Zener Current
5 mA
PMOS Maximum VGS
±20 V
Section 1: Design of Zener Bias Resistor (R1)
The resistor R1 supplies the required current to the Zener diode while limiting the current drawn from the 100 V supply.
Applying Kirchhoff's Voltage Law (KVL):
Therefore:
Substituting the design values:
Nearest standard value:
R1 = 18 kΩ
Power Dissipation of R1:
Voltage across R1: VR1 = 100 - 12 = 88 V
Power: PR1 = 88² / (18 × 10³) = 0.43 W
Select a 1 W resistor
Section 2: Design of Gate Pull-up Resistor (R2)
The pull-up resistor returns the PMOS gate to the source voltage when the NMOS is OFF.
Assume the gate pull-up current: IG = 1 mA
Using Ohm's law:
Selected value:
R2 = 100 kΩ
Power dissipation:
PR2 = 100² / 100k = 0.1 W
Select a 0.25 W resistor
Section 3: Capacitor Selection
The capacitor filters high-frequency switching noise and suppresses voltage transients across the PMOS gate.
Selected value:
C1 = 100 nF
Final Designed Component Values:
Component
Selected Value
R1
18 kΩ (1 W)
R2
100 kΩ (0.25 W)
Zener Diode
12 V
Capacitor
100 nF
The selected component values ensure safe PMOS gate operation and reliable switching over the 100 V supply range.
Notes: 2

## Slide 3
Simulation Results
LTspice Simulation Parameters:
  Supply Voltage = 100 V
  Input Pulse = 0–3.3 V
  Switching Frequency = 10 kHz (typical)
  Load = 1 kΩ resistive load
Waveforms Analyzed:
  Input Logic Pulse (0–3.3 V)
  NMOS Gate Voltage
  PMOS Gate Voltage
  Output Voltage
  Load Current
Simulation Observations:
  NMOS Response: The NMOS responds correctly to the 3.3 V logic signal, turning ON and OFF sharply with minimal delay.
  PMOS Gate Voltage Clamping: The PMOS gate voltage is clamped at approximately −12 V, protecting the MOSFET gate oxide from overvoltage conditions.
  PMOS Turn-ON: The PMOS turns ON completely when the input pulse is HIGH, allowing full conduction through the load.
  Output Voltage: The output voltage rises to approximately the supply voltage (100 V), confirming proper high-side switching operation.
  PMOS Turn-OFF: During the LOW input state, the PMOS gate returns to the source voltage (100 V), ensuring complete turn-OFF and zero load current.
  Switching Stability: The switching waveforms show stable operation with negligible overshoot, indicating effective gate protection and transient suppression by the Zener diode and capacitor.
  Gate Protection Verification: The Zener diode successfully clamps the gate-to-source voltage within the safe operating range (−12 V to 0 V), preventing gate oxide damage.
Key Performance Metrics:
  Gate-to-Source Voltage Range: −12 V to 0 V (within ±20 V limit)
  Switching Time: Fast response with minimal propagation delay
  Load Current: Reaches full value when PMOS is ON
  Transient Suppression: Effective noise filtering by C1 (100 nF)
Conclusion:
The simulation confirms that the circuit design meets all specifications and provides reliable high-side switching with proper gate protection across the 100 V supply range.
Notes: 3

## Slide 4
Advantages, Limitations and Transition to Circuit 2
Advantages:
  Simple and easy-to-understand circuit configuration
  Uses a small number of components (minimal BOM)
  Low implementation cost
  Fast switching due to the direct NMOS gate drive
  Suitable for high-voltage DC switching applications
  Easy to interface with 3.3 V microcontrollers
  The Zener diode provides reliable protection against excessive gate-to-source voltage
  Compact design with minimal PCB footprint
Limitations:
  No galvanic isolation between the controller and the high-voltage power stage
  The control circuit and the power circuit share a common ground, making the system susceptible to electrical noise and ground-loop currents
  Less suitable for electrically noisy industrial environments
  The microcontroller remains vulnerable to high-voltage transients and fault conditions
  Susceptibility to electromagnetic interference (EMI) from switching transients
  Ground-loop currents can degrade signal integrity in sensitive applications
  Not recommended for safety-critical applications requiring isolation
Why is Circuit 2 Required?
Although the general PMOS–NMOS driver performs reliable high-side switching, it lacks electrical isolation between the low-voltage controller and the 100 V power stage. In industrial applications, electromagnetic interference (EMI), switching transients, and ground-loop currents can affect the controller and reduce system reliability.
To address these critical issues, the next design introduces an optocoupler (PC817) between the controller and the PMOS gate driver. The optocoupler transfers the control signal optically, providing:
Complete galvanic isolation between the 3.3 V logic circuit and the 100 V power stage
Improved noise immunity against EMI and switching transients
Enhanced protection for the low-voltage control circuit from high-voltage faults
Ground-loop elimination through optical signal transfer
Safety compliance for industrial automation, PLC interfaces, and safety-critical switching applications
Next Steps:
Circuit 2 will demonstrate how optical isolation dramatically improves system robustness and reliability in harsh industrial environments, making it the preferred solution for mission-critical applications.
Notes: 4

## Slide 5
Circuit-02:PMOS High-Side Driver using Optocoupler
Introduction
In industrial control systems, the controller generally operates at a low voltage (3.3 V), whereas the load is powered by a much higher voltage (100 V). Directly connecting the controller to the high-voltage switching circuit may expose it to switching transients, electromagnetic interference (EMI), and ground-loop currents. To improve safety and reliability, an optocoupler (PC817) is introduced between the controller and the PMOS gate driver.
The optocoupler transfers the control signal through light, providing galvanic isolation between the low-voltage control circuit and the high-voltage power circuit. The PMOS transistor continues to function as the high-side switch, while the Zener diode limits the gate-to-source voltage to ensure safe operation.
Working Principle - OFF Condition (Input = 0 V)
  The LED inside the PC817 is OFF
  The phototransistor remains in the cut-off region
  No current flows through resistor R5
  The PMOS gate is pulled up to the source voltage through resistor R4
  Therefore, VGS = 0 V
  Since the gate-to-source voltage is zero, the PMOS remains OFF and the load is disconnected from the supply
Working Principle - ON Condition (Input = 3.3 V)
  The controller applies a 3.3 V signal to the optocoupler LED
  The LED emits infrared light
  The phototransistor inside the PC817 turns ON
  The PMOS gate is pulled towards ground through resistor R5
  The Zener diode clamps the gate voltage to approximately 12 V below the source voltage
  Therefore, VGS ≈ −12 V
  The PMOS turns ON and connects the 100 V supply to the load
Main Components
  PMOS transistor – High-side switching device
  PC817 optocoupler – Electrical isolation
  Zener diode (12 V) – Gate protection
  R4 – Zener bias resistor
  R5 – Collector (gate pull-down) resistor
  C2 – Noise suppression capacitor
Circuit Diagram Area
Space reserved for circuit diagram insertion
Notes: 5

## Slide 6
Circuit Design and Component Calculations
Design Specifications
Parameter
Value
High Voltage Supply
100 V
Logic Input
3.3 V
Zener Voltage
12 V
Optocoupler
PC817
Zener Current
5 mA
Optocoupler LED Current
10 mA
Section 1: Design of Zener Bias Resistor (R4)
The resistor R4 supplies sufficient current to the Zener diode while maintaining a stable gate reference voltage.
Applying Kirchhoff's Voltage Law:
VS = IR4·R4 + VZ
Therefore:
R4 = (VS - VZ) / IZ
Substituting:
R4 = (100 - 12) / (5 × 10⁻³)
R4 = 17.6 kΩ
Nearest standard value: R4 = 18 kΩ
Power Dissipation:
Voltage across R4: VR4 = 88 V
Power: P = 88² / 18k = 0.43 W
Choose a 1 W resistor
Section 2: Design of Collector Resistor (R5)
The collector resistor limits the collector current of the optocoupler transistor while providing sufficient gate drive current for the PMOS.
Applying KVL:
VZ = IC·R5 + VCE(sat)
Therefore:
R5 = (VZ - VCE(sat)) / IC
Assume:
  Collector current: IC = 10 mA
  Saturation voltage: VCE(sat) = 0.2 V
Substituting:
R5 = (12 - 0.2) / 10 mA
R5 = 1.18 kΩ
Nearest standard value: R5 = 1 kΩ
Power:
P = 11.8² / 1000 = 0.139 W
Select a 0.25 W resistor
Section 3: Optocoupler LED Resistor
To safely drive the LED inside the PC817:
Applying Ohm's Law:
RLED = (VIN - VF) / IF
Where:
  VIN = 3.3 V
  VF = 1.2 V
  IF = 10 mA
Substituting:
RLED = (3.3 - 1.2) / 10 mA
RLED = 210 Ω
Selected value: 220 Ω
Section 4: Capacitor Selection
To suppress switching transients and stabilize the Zener reference:
C2 = 100 nF
Final Designed Component Values
Component
Selected Value
R4
18 kΩ (1 W)
R5
1 kΩ (0.25 W)
LED Resistor
220 Ω
Zener
12 V
Capacitor
100 nF
These values ensure safe PMOS gate operation, reliable optocoupler switching, and effective electrical isolation.
Notes: 6

## Slide 7
Simulation Results
LTspice Simulation Conditions
  Supply Voltage = 100 V
  Logic Input = 0–3.3 V Pulse
  Optocoupler = PC817
  Zener Voltage = 12 V
  Load = 1 kΩ resistive load
Simulation Waveforms Analyzed
  3.3 V input pulse
  Optocoupler output (collector voltage)
  PMOS gate voltage
  Output voltage across the load
  Load current
Simulation Observations
1
Optocoupler Isolation: The optocoupler provides complete electrical isolation between the controller and the power circuit, with no direct electrical path between the two sides.
2
Phototransistor Switching: The phototransistor switches correctly in response to the LED input, demonstrating reliable optical signal transfer.
3
PMOS Gate Voltage Clamping: The PMOS gate voltage is clamped to approximately −12 V, ensuring safe operation within the ±20 V maximum rating.
4
PMOS Turn-ON: The PMOS turns ON fully when the optocoupler conducts, allowing complete connection of the 100 V supply to the load.
5
Output Voltage Response: The output voltage reaches the supply voltage (100 V) with minimal switching delay, confirming proper high-side switching operation.
6
Noise Immunity: Stable switching is achieved with reduced susceptibility to electrical noise, making the circuit suitable for industrial applications with EMI present.
7
Isolation Verification: The simulation confirms that the optocoupler successfully isolates the low-voltage control circuit from the high-voltage power stage, protecting the microcontroller from transients.
Key Performance Metrics
Gate-to-Source Voltage Range: −12 V to 0 V (within ±20 V limit)
Optocoupler Propagation Delay: Minimal (typical 2-5 μs for PC817)
Output Voltage: Reaches 100 V when PMOS is ON
Load Current: Full conduction when PMOS is ON
Isolation Voltage: Complete galvanic isolation between circuits
Noise Suppression: Effective filtering by C2 (100 nF)
Conclusion
The simulation confirms that the optocoupler-based PMOS driver successfully provides galvanic isolation while maintaining reliable high-side switching operation. The circuit demonstrates excellent noise immunity and protection for the microcontroller in industrial environments.
Notes: 7

## Slide 8
Advantages, Limitations and Transition to Circuit 3
Advantages
Provides complete galvanic isolation between the control and power circuits
Protects the microcontroller from high-voltage faults and transients
Excellent noise immunity, reducing the effects of EMI and ground loops
Reliable operation in industrial environments
Suitable for PLCs, embedded systems, and battery management applications
Maintains safe PMOS gate voltage using the Zener protection network
Eliminates ground-loop currents through optical signal transfer
Enhanced system safety and reliability for mission-critical applications
Limitations
Increased component count compared to the general PMOS–NMOS driver
Slight propagation delay due to the optocoupler (typically 2-5 μs)
Higher overall circuit cost due to optocoupler IC
Optocoupler performance may vary with temperature and device aging (CTR variation)
Requires continuous control signal to maintain output state
Power consumption increases due to LED drive current
Why is Circuit 3 Required?
The optocoupler-based PMOS driver successfully isolates the controller from the high-voltage power stage and improves system safety. However, the PMOS remains ON only while the control signal is continuously applied. In many industrial automation systems, it is desirable for the output to remain in its commanded state even after the control pulse has ended.
To meet this requirement, the next design introduces a transistor-based latching circuit. The latching circuit stores the output state using positive feedback, allowing the PMOS to remain ON after a short SET pulse and to turn OFF only when a separate RESET pulse is applied.
Key Benefits of Circuit 3 (Latching Circuit)
Memory-Based Switching: Output state is retained after the control pulse ends
Reduced Controller Workload: No need for continuous signal application
Minimized Drive Requirements: Lower power consumption from the control circuit
Pulse-Based Control: SET and RESET pulses instead of continuous signals
Industrial Automation Ready: Ideal for relay-like behavior in control systems
Safety-Critical Applications: Enables fail-safe designs with explicit RESET commands
Next Steps:
Circuit 3 will demonstrate how a latching circuit enables memory-based switching, allowing the PMOS to maintain its state independently. This design is essential for industrial control and automation systems where continuous drive signals are impractical or undesirable.
Notes: 8

## Slide 9
Circuit-03:PMOS High-Side Driver with Transistor Latching Circuit
The third proposed circuit incorporates a transistor-based SET–RESET latch with a PMOS high-side switch. Unlike the previous circuits, the PMOS remains ON after receiving a short SET pulse and is turned OFF only by a RESET pulse. This eliminates the need for a continuous control signal, reducing controller workload and improving energy efficiency.
Components Used
  PMOS – High-side switching device
  Q1 – SET transistor
  Q2 – Latching transistor
  Q3 – RESET transistor
  Zener diode (12 V) – Gate voltage protection
  R1 & R2 – Voltage divider network
  RB1, RB2 & RB3 – Base current limiting resistors
Working Principle: OFF State
  Q1, Q2, and Q3 remain OFF
  PMOS gate equals source voltage
  VGS = 0, therefore PMOS is OFF
Working Principle: SET Operation
  A 3.3 V SET pulse turns ON Q1
  Q1 provides base current to Q2
  Q2 saturates and establishes positive feedback
  The PMOS gate is pulled low
  The Zener diode limits VGS to approximately −12 V
  PMOS turns ON and remains ON after the SET pulse is removed
Working Principle: RESET Operation
  A RESET pulse turns ON Q3
  Q3 removes the base drive of Q2
  Q2 switches OFF
  PMOS gate returns to source potential
  PMOS turns OFF
Notes: 9

## Slide 10
Design Calculations (Part A)
Design Conditions
Supply Voltage: VS = 5 V to 100 V
Zener Voltage: VZ = 12 V
Case 1: VS < 12 V
Since VS ≤ VZ, the Zener diode remains OFF.
IZ = 0
Applying KVL:
Hence:
Gate voltage:
PMOS OFF Condition
Substituting:
Using:
  R1 = 500 kΩ
  VS = 5 V
  VCE = 0.2 V
  Vth = 4.2 V
R2 ≤ 71.42 kΩ
Therefore:
R2 = 70 kΩ
Selection of R1
Choose: R1 = 500 kΩ
At VS = 100 V:
  Voltage across R1: VR1 = 12 V
  Voltage across R2: VR2 = 88 V
Power dissipations:
  PR1 = 288 μW
  PR2 = 110.6 mW
Both are safely within a 250 mW resistor rating.
Summary of Part A Design
1
Maintain PMOS OFF condition when Q1 and Q2 are OFF
2
Provide stable gate reference voltage across the 5–100 V supply range
3
Ensure all resistor power dissipations remain within safe limits
4
Support reliable transistor switching for SET and RESET operations
Notes: 10

## Slide 11
Design Calculations (Part B) & Simulation Results
Zener Verification
Applying KCL:
IZ = 88/70k − 12/500k
IZ = 1.233 mA
Power:
PZ = 12 × 1.233 mA
PZ = 14.8 mW
A 500 mW Zener diode is selected.
Transistor Saturation Design
Q1 (SET Transistor)
RB1 ≤ 207.2 kΩ
Choose: RB1 = 100 kΩ
Power: 67.6 μW
Q2 (Latching Transistor)
RB2 ≤ 51 MΩ
Choose: RB2 = 100 kΩ
Power: 100 mW
Q3 (RESET Transistor)
RB3 ≤ 260.5 kΩ
Choose: RB3 = 100 kΩ
Power: 67 μW
Simulation Results
LTspice Simulation Conditions
  Supply Voltage = 5 V to 100 V
  SET Pulse = 3.3 V
  RESET Pulse = 3.3 V
  Load = 1 kΩ resistive load
  Zener Voltage = 12 V
Simulation Observations
  SET Pulse Response: Q1 turns ON with the SET pulse and initiates the latch by providing base current to Q2.
  Latch Holding: Q2 maintains the ON state even after the SET pulse is removed, demonstrating positive feedback operation.
  Gate Voltage Clamping: The PMOS gate voltage remains clamped near −12 V by the Zener diode, ensuring safe operation.
  Output Stability: The output remains ON until a RESET pulse activates Q3, demonstrating reliable memory-based switching.
  RESET Operation: Q3 successfully clears the latch by removing base drive from Q2, returning the PMOS to the OFF state.
  Wide Supply Range: The circuit demonstrates stable operation across the full supply range of 5–100 V.
  Transient Suppression: Switching transients are effectively suppressed by the Zener diode and gate protection network.
Key Performance Metrics
  Gate-to-Source Voltage Range: −12 V to 0 V (within ±20 V limit)
  Latch Holding Time: Indefinite (until RESET pulse)
  SET Pulse Duration: Minimal (microseconds)
  RESET Pulse Duration: Minimal (microseconds)
  Output Voltage: Reaches 100 V when PMOS is ON
  Load Current: Full conduction when PMOS is ON
  Power Dissipation: Minimal in latched state (no continuous drive)
Conclusion
The simulation confirms that the transistor-based latching circuit successfully implements SET–RESET memory functionality while maintaining safe PMOS gate protection across the entire 5–100 V supply range.
Notes: 11

## Slide 12
Design Verification, Advantages and Applications
Design Verification at VS = 100 V
IC1 = IC2 = 1.25 mA
IB1 = 26 μA
β·IB1 = 2.6 mA (greater than 1.25 mA) ✔ Q1 Saturates
IB2 = 0.993 mA
β·IB2 = 99.3 mA (greater than 1.25 mA) ✔ Q2 Latches
IC3 = 0.998 mA
β·IB3 = 2.6 mA (greater than 0.998 mA) ✔ Q3 Resets
Design Verification at VS = 5 V
IC1 = IC2 = 8.4 μA
β·IB1 = 2.6 mA (greater than 8.4 μA) ✔
IB2 = 43 μA
β·IB2 = 4.3 mA (greater than 8.4 μA) ✔
IC3 = 48 μA
β·IB3 = 2.6 mA (greater than 48 μA) ✔
All transistors achieve reliable saturation across the entire supply range, confirming design validity.
Final Component Values
Component
Selected Value
R1
500 kΩ
R2
70 kΩ
RB1
100 kΩ
RB2
100 kΩ
RB3
100 kΩ
Zener Voltage
12 V
Zener Power
14.8 mW
Advantages
  Latching operation using SET and RESET inputs
  Eliminates continuous controller drive requirement
  Safe PMOS gate protection with a 12 V Zener diode
  Reliable operation from 5 V to 100 V supply range
  Low power dissipation in all passive components
  Memory-based switching reduces controller workload
  Pulse-based control (SET/RESET) instead of continuous signals
  Suitable for industrial automation and embedded control systems
  Fail-safe design capability with explicit RESET commands
  Minimal propagation delay for fast switching response
Applications
  Industrial automation and PLC systems
  Motor control and relay replacement
  Battery management systems (BMS)
  Power distribution and load switching
  Solenoid and actuator control
  Emergency shutdown circuits
  Uninterruptible power supply (UPS) systems
  Renewable energy systems (solar, wind)
  Electric vehicle charging systems
  Safety-critical switching applications
Notes: 12

## Slide 13
Comparative Analysis and Conclusion
Comparative Analysis of the Three Driver Circuits
Parameter
Circuit 1 (General PMOS–NMOS)
Circuit 2 (Optocoupler)
Circuit 3 (Latching Driver)
Supply Voltage
5–100 V
5–100 V
5–100 V
Logic Input
3.3 V
3.3 V
3.3 V
High-Side Switching
Yes
Yes
Yes
Electrical Isolation
No
Yes
No
Latching Capability
No
No
Yes
Continuous Input Required
Yes
Yes
No
Controller Protection
Moderate
Excellent
Good
Noise Immunity
Moderate
High
High
Component Count
Low
Medium
High
Circuit Complexity
Low
Medium
High
Industrial Suitability
Good
Very Good
Excellent
Conclusion
The three PMOS high-side driver circuits demonstrate a progressive enhancement in functionality and capability.
Circuit 1 (General PMOS–NMOS Driver) provides a simple and economical solution for basic high-side switching applications. It offers direct 3.3 V microcontroller interface with minimal component count and low cost, making it suitable for non-critical applications with moderate noise environments.
Circuit 2 (Optocoupler-Based Driver) improves safety and reliability by introducing galvanic isolation between the low-voltage control circuit and the high-voltage power stage. The PC817 optocoupler provides excellent noise immunity and protects the microcontroller from switching transients and EMI, making it ideal for industrial environments with significant electrical noise.
Circuit 3 (Transistor-Based Latching Driver) extends the design by adding SET–RESET memory functionality, allowing the PMOS to remain ON after a short SET pulse without requiring continuous controller intervention. This eliminates the need for continuous drive signals, significantly reducing controller workload and power consumption.
Design Verification Summary
  Selected resistor values satisfy the PMOS OFF condition across the entire supply range
  All transistors (Q1, Q2, Q3) achieve reliable saturation at both 5 V and 100 V supply voltages
  All component power dissipations remain within safe limits
  The Zener diode provides effective gate protection (14.8 mW at 100 V)
  The circuit operates reliably from 5 V to 100 V supply range
Selection Criteria
  Choose Circuit 1 for cost-sensitive, non-critical applications with low EMI
  Choose Circuit 2 for industrial environments requiring galvanic isolation and high noise immunity
  Choose Circuit 3 for automation systems requiring memory-based switching and minimal controller workload
Final Recommendation
The transistor-based latching driver (Circuit 3) is the most suitable solution for modern industrial automation and intelligent power switching applications. It combines the benefits of all three designs: simple implementation, reliable operation, memory-based control, and excellent performance across the entire 5–100 V supply range. This makes it the preferred choice for mission-critical applications in industrial control, renewable energy systems, electric vehicle charging, and safety-critical switching scenarios.
Notes: 13

## Slide 14
Electronic Switch Matrix Overview & Objectives
Problem vs Solution
Problem: Relay Based
  ❌ Large Wiring
  ❌ Manual Operation
  ❌ Slow Switching
  ❌ Limited Expansion
Solution: Ethernet Based
  ✅ Remote Control
  ✅ GUI Based
  ✅ Fast Switching
  ✅ Scalable Architecture
Key Objectives
Remote Control via Industrial PC
Ethernet Communication Protocol
MOSFET High-Side Switching
SPI GPIO Expansion (MCP23S17)
Reliable Operation & Verification
Scalable Multi-Channel System
System Highlights
  Real-time control of crew module loads
  Galvanic isolation for safety
  CRC and checksum verification
  Modular architecture for expansion
  Industrial-grade reliability
Notes: 14

## Slide 15
Overall System Architecture
This diagram illustrates the hierarchical structure and data flow within the Electronic Switch Matrix system, from the user interface down to the controlled loads.
Key Components Description
Layer 1: User Interface
  Industrial PC with GUI
  Real-time monitoring and control
  Command generation
Layer 2: Communication
  Ethernet Module
  Protocol handling
  CRC verification
Layer 3: Control Logic
  Microcontroller (SPI Master)
  Command processing
  Device management
Layer 4: GPIO Expansion
  MCP23S17 SPI GPIO Expanders
  4 devices for 32 GPIO channels
  Each device controls 8 channels
Layer 5: Power Switching
  MOSFET High-Side Drivers
  Galvanic isolation
  100V load switching
Layer 6: Load Control
  Crew module subsystems
  Real-time switching
  Reliable operation
System Characteristics
  Modular and scalable architecture
  Real-time communication
  Redundancy capability
  Industrial-grade reliability
Notes: 15

## Slide 16
Complete System Design Flow & Implementation
Notes: 16

## Slide 17
Communication Flow & Protocol Frame
Communication Sequence
① GUI Command Generation
② Ethernet Packet Creation
③ Ethernet Module Reception
④ CRC Verification
⑤ Microcontroller Processing
⑥ SPI Command Generation
⑦ MCP23S17 Reception
⑧ GPIO Output Update
⑨ MOSFET Activation
⑩ Load Switching
⑪ Status Read Back
⑫ ACK Generation
Application Frame Format
Frame Structure:
Field
Value
SOF (Start of Frame)
AA
Command
01 (ON) / 00 (OFF)
Device ID
00-03
Channel
00-07
Data
ON/OFF
Checksum
XX
EOF (End of Frame)
55
Frame Details
Frame Explanation
  SOF identifies frame start
  Command specifies ON/OFF operation
  Device ID selects MCP23S17 (0-3)
  Channel selects GPIO pin (0-7)
  Data contains the control value
  Checksum ensures data integrity
  EOF marks frame end
Key Features
  Simple and efficient protocol
  CRC and checksum verification
  Device and channel addressing
  Real-time command execution
  Status feedback capability
Notes: 17

## Slide 18
Channel Activation & SPI Transaction
Channel Activation Sequence
① GUI Selects Channel
② MCU Receives Command
③ Device Selection (MCP2)
④ SPI Control Byte = 44H
⑤ Register Address = 13H
⑥ GPIO GPB1 = HIGH
⑦ MOSFET Gate Driven
⑧ Load Turns ON
⑨ GPIO Read Back
⑩ Status Verification
⑪ ACK Sent to GUI
SPI Register Operation
Initial State
GPIOB = 10100000 (A0H)
Bit Modification
10100000 OR 00000010 = 10100010 (A2H)
SPI Write
  Device: MCP2
  Register: GPIOB (13H)
  Data: A2H
GPIO & Timing
GPIO Output
GPB0=0, GPB1=1✓, GPB2=0, GPB3=0
GPB4=1, GPB5=0, GPB6=1, GPB7=0
SPI Signals
  SCK: Serial Clock
  MOSI: Command
  MISO: Status
  CS: Chip Select
Timing
  SPI Clock: 1 MHz
  Transaction: ~10 μs
  GPIO Update: Immediate
  MOSFET: <1 μs
Notes: 18

## Slide 19
Reliability, Verification & Conclusion
Verification Checks
  CRC Verification - Ethernet frame integrity
  Checksum Validation - Application frame verification
  SPI Verification - Serial communication validation
  GPIO Read Back - Output status confirmation
  ACK Generation - Command completion confirmation
  Error Handling - Automatic retry mechanism
  Status Logging - Transaction recording
  Fail-Safe Design - Safe operation guarantee
System Advantages
  ⚡ Fast Switching - Microsecond response
  🛡 Reliable Operation - Multi-layer verification
  📡 Ethernet Communication - Remote control
  📈 Scalable Architecture - Easy expansion
  🔄 Modular System - Independent components
  ✔ Industrial Grade - Mission-critical reliability
  🔒 Galvanic Isolation - Safety protection
  📊 Real-time Monitoring - Live status feedback
Overall Workflow
GUI Command → Ethernet → MCU → SPI → MCP23S17 → MOSFET → Load → Status → GUI Update
Conclusion
The Electronic Switch Matrix system provides a robust, scalable, and reliable solution for remote control of crew module loads. With multiple verification layers, real-time communication, and industrial-grade components, the system ensures safe and efficient operation in mission-critical applications. The modular architecture allows for easy expansion and maintenance.
Notes: 19

## Slide 20
Evolution of Semiconductor Devices for Industrial High-Side Drivers
Technology Evolution Diagram
This diagram illustrates the progressive advancement in semiconductor transistor technologies.
Planar MOSFET
Traditional flat-channel device
FinFET
3D fin channel for better control
GAAFET
Gate-all-around for improved scaling
CFET
Stacked devices for density gains
Evolution of Transistor Technologies (Comparison Table)
Technology
Structure
Industrial Advantages
Planar MOSFET
Single planar channel with gate on the top surface
Simple fabrication, low cost, widely used in conventional industrial power converters
FinFET
Vertical fin-shaped channel with the gate surrounding three sides
Better electrostatic control, lower leakage current, reduced effective RDS(on), improved switching efficiency, higher reliability
GAAFET (Gate-All-Around FET)
Gate completely surrounds the nanosheet or nanowire channel
Superior gate control, lower leakage current, higher drive current, improved power efficiency, excellent scalability for advanced industrial ICs
CFET (Complementary FET)
Vertically stacked NMOS and PMOS transistors
Highest integration density, compact chip area, reduced parasitic capacitance, improved switching speed, enhanced power density
Industrial Perspective
The evolution from Planar MOSFET → FinFET → GAAFET → CFET represents continuous improvements in device performance:
  ✔ Lower effective channel resistance
  ✔ Reduced conduction losses
  ✔ Lower leakage current
  ✔ Faster switching speed
  ✔ Improved thermal performance
  ✔ Higher reliability
These technologies are well-suited for next-generation industrial automation and power electronics applications.
Key Performance Improvements
Planar MOSFET
  Baseline technology
  Cost-effective
  Established manufacturing
FinFET
  30-40% reduction in leakage
  Improved gate control
  Better switching efficiency
GAAFET
  50-60% lower leakage
  Higher drive current
  Superior scalability
CFET
  2x integration density
  Reduced parasitic effects
  Highest performance
Notes: 20

## Slide 21
Future Scope for Industrial High-Side Driver Circuits
Future Research Directions
Technology Enhancements:
  Replace Planar MOSFET with FinFET/GAAFET/CFET
    Improved switching performance
    Enhanced overall efficiency
    Better thermal management
  Develop Integrated Gate-Driver IC
    Advanced semiconductor technologies
    Compact industrial applications
    Reduced PCB footprint
  Incorporate SiC/GaN Power Devices
    Higher-voltage operation
    Higher-frequency switching
    Improved power density
Protection & Integration:
  Integrate Industrial Protection Features
    Overcurrent protection (OCP)
    Overvoltage protection (OVP)
    Thermal shutdown (TSD)
    Short-circuit protection (SCP)
  Optimize PCB Layout
    Minimize electromagnetic interference (EMI)
    Improve electromagnetic compatibility (EMC)
    Reduce parasitic effects
  Enable Industry 4.0 Features
    IoT-based remote monitoring
    Predictive maintenance
    Real-time fault diagnostics
Expected Industrial Benefits
Performance Metrics:
  ⚡ Lower RDS(on)
    Reduced conduction losses
    Improved efficiency
  🔄 Faster Switching
    Higher frequency operation
    Better power conversion
  ❄️ Enhanced Thermal Management
    Lower leakage current
    Improved heat dissipation
System Benefits:
  📦 Higher Power Density
    Compact circuit implementation
    Reduced component count
  🛡️ Increased Reliability
    Extended system lifetime
    Mission-critical performance
  🌐 Industry 4.0 Ready
    Remote monitoring capability
    Predictive maintenance
    Smart diagnostics
Application Domains
The proposed PMOS high-side driver is suitable for:
  ✔ Industrial automation and PLC systems
  ✔ Motor drives and servo control
  ✔ Battery management systems (BMS)
  ✔ Renewable energy converters (solar, wind)
  ✔ Electric vehicle power electronics
  ✔ Robotics and smart manufacturing
  ✔ Uninterruptible power supply (UPS)
  ✔ Power distribution systems
Conclusion
Future development of the proposed PMOS high-side driver can leverage FinFET, GAAFET, and CFET technologies to achieve:
  Higher efficiency and improved reliability
  Greater integration and compact design
  Combined with SiC/GaN devices for advanced performance
  Industry 4.0 connectivity for intelligent monitoring
  Support for compact, intelligent, and high-performance industrial power-switching solutions
Vision:
Next-generation industrial power electronics with enhanced performance, reliability, and intelligence through advanced semiconductor technologies and IoT integration.
Notes: 21